Safe Work Method Statement

| Job Safety Analysis worksheet |
| --- |
| Name of employer: |  | Date: |  |  |
| Workplace address: |  |  |  |  |
| Overall task: | Working at heights |  |  |  |
| Activity | Potential hazards/risks | Control measures | Who is responsible? |
| Training | Untrained workers may not be aware of hazards that could affect themselves or others. | Provide company induction, site induction and task training and certification as required. | Principal and contractor working at heights |
| Temporary access to heights | A fall from a ladder or other temporary access may injure workers. | An industrial grade ladder should be used up to 6 m. Secure the ladder safely at a 4:1 pitch. The ladder must extend 900 mm+ past any safe step-off point. An access tower should be used by heights above 6 m. | Contractor working at heights |
| Working at heights over 2 m | A fall or slide from a work platform may injure workers. | Work from a safe work platform. Provide fall protection over heights of 2 m. Provide roof guard rails for roof edges if working on roofs. All scaffolds and working platforms must comply with AS/NZS 4576 or AS 6001. Protective non-slip footwear should be worn. | Contractor working at heights |

| Activity | Potential hazards/risks | Control measures | Who is responsible? |
| --- | --- | --- | --- |
| Working from ladders | A fall from a ladder may injure workers. | Only insulated ladders are to be used for electrical work. Only light duty work can be done where one hand is required to carry out work. Workers are not to stand any higher than the third top rung. Industrial grade ladders should be used up to 6 m. Secure the ladder safely at a 4:1 pitch. | Contractor working at heights |
| Other workers working below or near workers who are working at heights | An object could fall and injure other workers below you. | Prevent workers from working below other workers, where falling objects are possible. Provide kick boards to prevent objects falling. | Contractor working at heights |
| Working with electric power tools | Workers could be electrocuted. | All electrical equipment should be checked and tagged every three months. Earth leakage protection should be provided. Multi-plug outlet devices should be up to industrial standards and must comply with AS 3105. Electrical leads should be clear of the ground and water. No green sheathed leads are to be used. Temporary switchboards are to be set up correctly. | Contractor working at heights |

| Activity | Potential hazards/risks | Control measures | Who is responsible? |
| --- | --- | --- | --- |
| Working near overhead powerlines | If a worker, plant or material come into contact with powerlines, the worker could be electrocuted. If scaffolding is within 5 m vertically and 4.6 m horizontally from powerlines on poles or plant within 3 m of powerlines on poles then additional precautions need to be taken. | Identify where the powerlines are and provide warning signs if work is required in the 'No go zone'. Isolate the power if possible. If this is not possible: fit warning tiger tails to the powerlines obtain written permission to work in the area from the electricity supply authority complete a risk assessment and hold a site meeting provide a qualified spotter. | Contractor working at heights |