Demolition daily checks

The following must be checked daily.

Make sure that:

all openings and elevated free edges are properly guarded

temporary hoardings, bracing, shoring and propping is tight and secure and in place as required to protect both workers and the public

all potential fire and safety hazards are eliminated

disconnected services are secured

all hazardous materials are removed or covered as required by OHS legislation

partly demolished elements are stabilised and loose materials are secured against bad weather

emergency access routes are clear of debris

all boundaries are secured against unlawful entry

footpaths and public access are clear of demolished materials

any hazards are properly lit, guarded and marked

demolished materials have not been left on any floor or structure if their weight exceeds the safe carrying capacity of the floor or structure

no structure or part of a structure is left in such a condition that it may become dangerous, such as collapse due to wind or vibration.