Building Act 1993
Building (interim) Regulations 2005
Regulation 1507(a)

Certificate of compliance – design

To: Relevant building surveyor

Postal address:	PO Box 888

GUNDAGAI	Postcode: 5678

From:

Building practitioner: Mr Peter Goodright	Category/class:

Postal address:	PO Box 42
YARCK	Postcode: 1234

| Property details |
| --- |
| Customer address: | 123 Country Lane | City/suburb/town: | Yarck |
| Lot(s) | N/A | LP/PS: | N/A | Volume: | N/A | Folio: | N/A |
| Crown allotment: | N/A | Section: | N/A | Parish: | N/A | Country: | N/A |
| Municipal: | Strathbogie |  |  |  |  |

Compliance:

I did not prepare the design, however, I certify that the design described as:

•	6 m span x 9 m O/A length x 2.7 m eaves height building, consisting of 3 bays at 3 m frame spacing produced by the multibuild building design programme (previously certified by me)

•	complies with the following provision of the regulations **for commercial use part B1 of Volume 1 BCA 2005, for domestic use includes BCA part 3.1.1 of volume 2 BCA 2005 and the following Australian Standards: AS/NZS 4600, AS 3600, AS 1170.1 and .2, AS 2870.

Design documents

Drawing nos:	Prepared by:	Date
PQ&R structural design drawing	PQ&R Building Systems	30/08/2007
for this project, pages 1 to 5

| Signature: |  | Date: | 30/08/2007 |
| --- | --- | --- | --- |
| Signed building practitioner | Mr Peter Goodright |  |  |

Registration No: BR 2468 VIC

Building permit

Building Act 1993
Building Interim Regulations 2005
Regulation 313

Permit no: BS-1234-2007123/4

Issued to:

Owner/agent:	A Lander	Phone:	9876 1234
	22 Block Place
	SITEVILLE   VIC   3131

Address for serving or giving of documents:

Contact:	A Lander	Phone:	9876 1234
	22 Block Place
	SITEVILLE   VIC   3131

Property details:	123 County Lane, Yarck 3777	Site area m2:	69278
Title details:	Ca:20B Sec: E Vol: 7442 Fol: 563	Property number	13579
	Buildright Shire Council

Builder:	As above

Practitioners	Registration	Category/class
Winter Mathis	EC5678	Engineer (documents only)
Spring George	VIC/04/005	5-star Energy rating
Summer Leo	EC1234	Engineer (documents only)

Details of relevant planning permit (if applicable)

The issuer or provider of the required insurance policy is:	Owner builder

Details of relevant planning permit (if applicable)

Planning permit no:	P2007/111	Planning permit date:	24/03/2007
Nature of building work:	Construction of dwelling	Total new floor area m2:	187
	and garage
Stage of building work:	All	Cost of building works:	$171,450.00
Part of building:	All parts	BCA classification:	1A and 10A

Inspection requirements: The mandatory notification stages are:

inspection of footings (shed)
inspection of pre-slab
inspection of framework
inspection of occupancy permit

Occupation or use of building: An occupancy permit is required prior to use of occupation

Commencement:	Building work must be commenced by:	15/05/2007
Completion:	And must be completed by:	15/05/2008

Municipal building surveyor:	David Rightbuild	Registration no:	BS1234

| Signature: |  | Date: | Monday 15 May 2007 |
| --- | --- | --- | --- |